## Slide 1
WIRESHARK WLAN
Read Block Ack behavior at a glance
A screenshot-led guide to sessions, bitmap evidence, agreement boundaries, and capture limits.
Real-world captures · current v0.0.3 behavior

## Slide 2
ORIENTATION
Real captures drive every example
Static and interactive views are derived from local 802.11/radiotap captures.
02
Normal progress 29 BA · 5 BAR · 4.4 s
Persistent holes 21 BA · 20 lifetimes
Sequence wrap 4086 … 4095, 0 … 10
Primary source: /Users/yujuiwu/code/debug/WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap

## Slide 3
ORIENTATION
A bitmap is evidence—not a loss verdict
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap
03
A bitmap zero means “no ACK observed here.”
A captured MPDU means “the sniffer saw it.”
Correlate both before drawing a conclusion.

## Slide 4
GETTING STARTED
Open all sessions—or follow one BA
Actual local Wireshark development build; UI-only example.
04
Wireless → WLAN Block Ack Graph
Analyze → Follow → WLAN Block Ack Session Graph

## Slide 5
GETTING STARTED
Choose the BA pair, then the TID
UI controls shown with a local review capture; interpretation examples use real captures.
05
BA pair (TA → RA) Sorted by total BA count across all TIDs.
TID Sorted by BA count; each item shows BA and BAR totals.
Direction follows the BA response. BARs and matching QoS Data are normalized into that session.

## Slide 6
READ THE NORMAL CASE
Read time first, then sequence
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · normal 4.4 s excerpt
06
Y · sequence number labels modulo 4096
X · capture-relative time

## Slide 7
READ THE NORMAL CASE
Blue starts the window; orange ends it
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · normal excerpt
07
●
BA starting sequence (SSN)
●
Window upper bound
Upper bound = SSN + number of bitmap sequence positions

## Slide 8
READ THE NORMAL CASE
Shape separates BARs from captured MPDUs
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · normal excerpt
08
△
BAR starting sequence
◆
Captured QoS Data MPDU
Gold proves capture presence—not receiver delivery.

## Slide 9
READ THE NORMAL CASE
Green dots are the BA bitmap’s set positions
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · interactive normal replay
09
Clear “Show bitmap set” when dense green evidence hides the core traces.

## Slide 10
READ THE NORMAL CASE
A healthy session climbs like a staircase
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · 29 BA · 5 BAR · 213 matching MPDUs
10
SSN 4 → 101 in 4.4 seconds

## Slide 11
USE THE CONTROLS
Labels show SSN; deltas show BA spacing
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · normal excerpt
11
SSN labels wrapped 12-bit values
BA time deltas 960.2 ms · 516.7 ms · 421.4 ms

## Slide 12
USE THE CONTROLS
Click a marker to jump to its packet
Actual local Wireshark graph UI; click behavior is packet-linked.
12
The detail line reports: • frame • wrapped + unwrapped sequence • bitmap or lifetime facts
Wireshark moves the packet list to the source frame.

## Slide 13
USE THE CONTROLS
Zoom selects; Drag preserves context
Actual local Wireshark graph UI; the real-data examples use the same controls.
13
Zoom Drag a rectangle across the plot.
Drag Pan the current viewport.
Wheel scales · Reset Graph refits the session

## Slide 14
USE THE CONTROLS
The summary follows the visible range
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · interactive normal replay
14
DISPLAYED SPAN
EVENTS CURRENTLY IN VIEW

## Slide 15
DIAGNOSE EVIDENCE
Gray dots mark SSN advances without BA ACK
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · normal excerpt · 35 gap positions
15
●
No BA ACK before SSN advance
It is missing BA evidence. It is not proof that the MPDU was transmitted or lost.

## Slide 16
DIAGNOSE EVIDENCE
A hole is a zero before the highest set bit
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · persistent-hole excerpt · 228 holes
16
Trailing zeros are not plotted.

## Slide 17
DIAGNOSE EVIDENCE
Persistent-hole spans expose aging
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · 21 BA over 44.65 s
17
20 lifetimes across consecutive covering BAs
Select a square endpoint to see whether the hole was later ACKed, passed by SSN, interrupted, or still active.

## Slide 18
DIAGNOSE EVIDENCE
Green and red crosses mean different evidence
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · classification is scoped to one agreement epoch
18
× Green cross An earlier BA in this agreement explicitly set the sequence.
× Red cross No earlier observed set-bit evidence exists in this agreement.
Neither color, by itself, proves transmission or loss.

## Slide 19
DIAGNOSE EVIDENCE
Gray marks an explicit BA FCS error
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · bad-FCS frames 29412 and 29438
19
2 bad-FCS BAs 40.884 ms apart
Keep the sample for chronology—but treat its bitmap, holes, and labels as untrusted evidence.

## Slide 20
DIAGNOSE EVIDENCE
ADDBA and DELBA bound the agreement
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · frames 12118, 12120, and 12192 · TID 0
20
ADDBA OK starts a new agreement and clears prior history
DELBA ends the agreement and clears history
Request and rejected response are context only.

## Slide 21
DIAGNOSE EVIDENCE
4095 → 0 is wraparound—not a reset
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · 20 BA · SSN 4086 … 4095, 0 … 10
21
Internal progression stays continuous: 4095, 4096, 4097 …
A backward sample that cannot extend the ACK frontier starts an inferred epoch only when wrap logic cannot explain it.

## Slide 22
TROUBLESHOOT
Why a valid WLAN frame may not appear
Use the packet fields and capture-total counters before assuming a plotting defect.
22
Wrong BA response direction
Different TID or session epoch
Not a supported BA/BAR format
Malformed or incomplete dissection
No usable bitmap / address / TID fields

## Slide 23
TROUBLESHOOT
The 32-bit BA-looking record is corrupt
Real capture audit: pcie-12186-1127-05-oid-capture-time-adjusted-2nd-half.pcapng
23
Field
Observed value
Frame / time
44354 / 40.298502 s
Decoded type
Multi-STA Block Ack response
TA → RA
e1:24:a9:9c:d3:30 → 11:12:b4:5f:eb:56
Entry
AID 0x722 · TID 2 · SSN 680
Bitmap
e6084730 · 4 bytes / 32 bits
Trust
Radiotap Bad FCS + Bad PLCP
Do not treat this as a valid 32-bit BA session.
Current graph excludes Multi-STA BA. The implausible addresses and explicit radio errors support that decision.
Matching reverse-direction BARs: 0

## Slide 24
REFERENCE
Which BA formats the graph accepts
Current code path; primary WQCPC capture verifies Compressed BA only.
24
Format
Graph treatment
Real-case status
Basic BA
Supported
Code-checked
Compressed BA
Supported
2,217 BA verified
Extended Compressed
Supported
Code-checked
Multi-TID
Supported
Code-checked
Multi-STA / GCR
Excluded
Unsupported counter
The BA window upper bound reflects the number of sequence positions represented—not simply the byte count.

## Slide 25
WORKFLOW
Turn a long capture into one interval
Real capture: WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap · normal replay used as the focused interval
25
→
1 · choose pair + TID 2 · enable only the needed layers 3 · rectangle-zoom
4 · read the live summary 5 · click markers back to frames 6 · check FCS and capture visibility

## Slide 26
WORKFLOW
Use the same six questions every time
A repeatable interpretation sequence reduces false loss conclusions.
26
1 · Pair + TID
2 · Agreement epoch
3 · SSN + BAR
4 · Bitmap history
5 · MPDU + retry evidence
6 · FCS + capture quality

## Slide 27
LIMITATIONS
Capture quality sets the confidence ceiling
Examples are capture evidence; receiver-internal delivery state is not directly observed.
27
Explicit bad FCS Decoded, but untrusted
Bitmap zero No ACK observed—not proven loss

## Slide 28
APPENDIX
Verified cases behind these examples
Local capture extraction, renderer replay, and current source inspection.
28
Case
Verified result
Capture inventory
310,253 packets · radiotap IEEE 802.11 · 3,700.708032 s
BA / BAR extraction
2,217 compressed BA · 234 compressed BAR
Normal replay
29 BA · 5 BAR · 213 MPDU · 35 ACK gaps
Persistent replay
21 BA · 444 set · 228 holes · 20 lifetimes
Wrap replay
4086 … 4095, 0 … 10 stays continuous
Bad-FCS classification
Frames 29412, 29438, 29771, 29815
Agreement lifecycle
Frames 12118 request · 12120 OK · 12192 DELBA
No dedicated automated GUI interaction test is claimed; visual behavior was inspected from the generated deck and source-backed captures.

## Slide 29
APPENDIX
Capture index and control reference
Full source paths are retained for local reproduction.
29
Use
Capture / asset
Primary behavior
…/WQCPC-13082/20260421_062701_20M_CH6_DONT_CARE.pcap
32-bit audit
…/PCIE-12186/1127/05-oid-capture/pcie-…-2nd-half.pcapng
Static views
doc/wsug_src/images/ws-wlan-ba-real-{normal,holes,wrap}.png
Interactive replay
doc/wlan_block_ack_graph.html
Mouse Drag · Zoom · wheel · axis drag
Keyboard Z · X/Shift+X · Y/Shift+Y
Output Reset Graph · Save As PDF/PNG/BMP/JPEG

## Slide 30
WLAN BLOCK ACK GRAPH
Start with the session. End with the evidence.
Pair + TID → agreement epoch → SSN/BAR → bitmap history → MPDU/retry evidence → FCS quality
A zero is evidence to investigate—not a verdict.